## Slide 1
A tool kit to take you from the development of an ASIC Pad Ring Pad Ring Explorer to a Package Wire Bond fan out pattern Wire Bond Explorer.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top
Notes: Windytop

## Slide 2
The Basic version is for the engineers who only need limited functionality to place a die onto a substrate or PCB.
The Advanced version adds more functionality and editing capability, a command language that can be used for scripting, the ability to add a stacked Die to the project at any location and rotation and a 3D LIQ viewer.
The Full version includes the Pad Ring Explorer to aid in the design and analysis of ASIC Pad Rings.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 3
This tool has 3 parts. The Netlist tool, the Die tool and the Wire Bond fan out tool.
The Netlist tool allows you to read in or create a netlist as the starting point of a design.
The Die tool allows you to edit the position and size of the bond pads on a die as well as establishing the size of the die itself.
The Wire Bond tool is used to generate the fan out pattern for the design.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top
Notes: Windytop

## Slide 4
Once a netlist has been loaded, the specific part from the parts in the netlist is selected as the target part for the project.
The netlist can be sorted either by RefDes or Net name. Complete statistics are also displayed.
This is the first step in the design process. If a netlist is not available but a pin list or LIQ file of a die is, the netlist will be generated from the pin list or LIQ file.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 5
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 6
Creating and editing the die pads is the second step in the project. If a die picture is available it can be imported and used to guide the placement and sizing of die pads.
Automatic die pad creation can be done if you know the size and spacing parameters of the die pads.
Once all the pads have been defined a datasheet can be generated with all the statistics along with a picture of the die.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 7
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 8
This tool generates the wire bond fan out from a set of rules that define the placement tiers, pad to pad and pad to wire spacing.
The die attach pad can also be edited using the Attach Pad Editor.
Once the fan out has been generated it can viewed using the 3D LIQ Viewer where the wire parameters can be manipulated.
The Stacked Device Editor allows you to add a second device on top of the base die.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 9
As with the Die tab a data sheet can be generated from the fan out showing die, wire bonds and the substrate attach points.
If multiple bond sites are required the Bond Site Editor and Split Join tools can be used to manipulate the attach points on either the die and or the substrate.
Complete editing features allow you to manually edit the attach points on the substrate.
From the 3D LIQ Viewer, you can get a rough extraction of the LR of the wires using the LR Estimator.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 10
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 11
This tool lets you view a project in 3D by reading in the LIQ file generated by the Wire Bond Explorer.
The wire loop height and extensions can be modified allowing customization of the wires.
The LR Estimator will do a rough extraction of the wires.
Screen shots can also be taken for presentation.
Individual or groups of wires can also be highlighted for closer inspection.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 12
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 13
The fan out process is controlled by the Fan Out dialog box, DRC parameters in the Properties and the Assign tool.
The Tiers are first defined.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 14
Once the placement tiers or rings have been defined the substrate bond pads are defined.
This included the orientation, end cap shape and the size.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 15
Finally the DRC rules for the fan out process are set for each Tier.
The wire with, pad to pad, pad to wire DRC rules are entered.
The Max Wire Length and Max Wire Angle are used for post processing analysis.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 16
The Assign tool is used to assign the pads to specific tiers. It can also be used to move pads from one tier to another or clear the design and try another placement.
If a group of selected pads are placed on multiple tiers they will alternate between the tires.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 17
Now that the pads have been placed the Wire Bond tab looks like this.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 18
The Fan Out tool is used to control the Fan out process.
Here you select which pads are going to be used as well as how the process runs.
The Effort options tells the tool how hard to work to keep the DRC rules enforced. If you want to do a quick and dirty design just to see what it might look like set the Effort to a low number. For the best accuracy set the Effort to a high value.
Once completed, the statistics are displayed at the bottom of the dialog box.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 19
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 20
Once the Fanout is completed the Wire Bond tab will look something like this.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 21
The Die Attach editor is used to define the Die Attach pad and it’s connectivity to the inner most ring if that is desired.
The attach style can be Solid, Hatched or None.
If Hatched, the number of rows, columns and width are used.
The Die Attach Margin defines any over or under sizing to be done.
The Inner Ring Attach defines the connectivity to the inner ring and how it is done.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 22
The width of the Ring Attachment is defined as well as the number of spokes for the attachment.
The attachment can be made either Orthogonal or Radial.
As the mouse is moved over a selected parameter the quick view will display the parameter being used.
Once the parameters are Applied they will be reflected in the design.
The Die Attach Pad editing can be done at any time during the design process.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 23
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 24
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 25
These tools are used to split a single Die Pad into multiple segment for the purpose of doing multiple wire bonding. For a single pad such as a power or ground pad.
The Split / Join tool allows you to select a CBP and the number of segments. You can optionally Join a previously split CBP back into one pad.
If the Substrate Bond Pads are to be overlapped than the Merge SBPs box is checked.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 26
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 27
The Bond Site Editor is used to manipulate the position of the Bond Attach points on both the die and the substrate.
There are 2 tabs. One for the Component Bond pads to the Substrate Bond Pads and another one for use with a stacked device. Base Die Pad to Stacked Device Pad.
X and Y offsets are defined and then applied. Once Applied the changes will be seen.
You can select multiple pads or all pads on any given tier .
If you have a Split Pad that is merged the effect is to have multiple bond sites on one SBP.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 28
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 29
Split CBP with 3 segments and Merged SBPs
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 30
If you want to have Split Rings in your design you can use this editor to split the Power or Ground Rings into several different segments.
This is done by selecting the tier and edge to be split along with the Split Gap value.
The Add button will add a split on the selected side . The Remove button will remove a selected split.
The splits can be edited and moved using the mouse or selecting them and using the arrows.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 31
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 32
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 33
To add a Stacked Device you first select the LIQ file for the device. This will load the die and place it in the center if the Base die.
Using the Arrow keys and Rotation buttons the die can be located any place on the base die and at and angle of rotation.
The Pick and Place option allows you to edit the wire order the Fanout process.
The stitch Pad to Pad is used to connect the Stacked Device to the Base Die.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 34
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 35
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 36
Every time you execute a command it is recorded in a .kmd file. These commands can be executed at any time either by manually entering them in the command line or running the script using the Run command.
This is handy if you have set up parameters that you want to automatically run for every design.
The .kmd file can also be edited with lines you don’t want executed commented out with an “*” at the beginning of a line.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 37
A Wait command can be inserted at any point to enter a wait state for n seconds.
There is a special command “FILIQAPLA” File ImportLIQAsPinListAuto. This is the one command available to the Basic Package.
The command are executed sequentially and nesting is not allowed at this time.
A sample command file is listed below. Also refer to the CommandList.pdf
FO the command >FanOut the description. Any parameters follow the = sign and separated by : or a space. Pairs are enclosed in (n1:n2).
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 38
RunLoFO>FanOut
*FOCB>FanOutClearBefore=No
FOCB>FanOutClearBefore=Yes
*FOCG>FanOutCenterGroup=No
FOCG>FanOutCenterGroup=Yes
FOCA>FanOutCenterAngle=No
*FOCA>FanOutCenterAngle=Yes
*FOL>FanOutLeft=No
FOL>FanOutLeft=Yes
*FOB>FanOutBottom=No
FOB>FanOutBottom=Yes
*FOR>FanOutRight=No
FOR>FanOutRight=Yes
*FOT>FanOutTop=No
FOT>FanOutTop=Yes
*FOS>FanOutSelected
FOE>FanOutEffort=5
FOA>FanOutAll
*FOAC=No
FOL>FanOutLeft=Yes
*FOB>FanOutBottom=No
FOB>FanOutBottom=Yes
*FOR>FanOutRight=No
FOR>FanOutRight=Yes
*FOT>FanOutTop=No
FOT>FanOutTop=Yes
*FOS>FanOutSelected
FOE>FanOutEffort=5
FOA>FanOutAll
*FOAC=No
FOAC=Yes
FOKP>FanOutKeepPinOrder=No
*FOKP>FanOutKeepPinOrder=Yes
FOKE>FanOutKeepEdges=No
*FOKE>FanOutKeepEdges=Yes
FOTO>FanOutTierOverRun=10
FOEXE>FanOutExecute
FOCANCEL>FanOutCancel
FanOut1.kmd
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 39
This feature exists in both the 3D LIQ Viewer and the LR Estimator which is accessed from the viewer.
If only one die is used, the Stack device and wires are not highlighted in the preview.
The selection of the material, wire diameter and frequency are used in the LR calculations.
The loop heights and extensions define the wire shape.
The default values are set to the die thickness.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 40
Custom settings override the default settings
In the case of a stacked device the Edge of Base Die option will extend the wire to the edge of the base die before it starts the angle downward to the SBP.
Apply will alter the 3D view taking the new settings into account.
Set up parameters can be saved and loaded for future projects.
Reset will set all parameters to the default state.
The LR Estimator button will open the estimator.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 41
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 42
The LR Estimator looks like the Wire Bond Setup tool.
All the parameters are the same and passed into the tool from the Viewer in a .lr file.
They can be modified here if you wish to see the results of different settings than saved and loaded back into the Wire Bond Setup for viewing in the 3D Viewer.
Once the data is Processed it is displayed and saved in a .lr.doc file
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 43
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 44
The Properties dialog box contains all the set up parameters for the project.
The Top of the tree lists the project options.
The System branch lists all the paths to other tools.
The Project branch lists the files used in the project as well as the chip used, Pin ID and Font Size
The Net List branch has all the details about the netlist
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 45
The Die branch contains all the information about the Die including the die size and all the pads on the die.
The Fan Out branch, as you already have seen, contains all the parameters used in the fan out process.
Any properties that are highlighted in white can be edited.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 46
Global Parameters.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 47
Tool Paths to system tools.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 48
Project Files and Settings.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 49
Net List Statistics
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 50
Lists the total number of components in the netlist and the component selected for the project.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 51
Lists the all the Parts in the Netlist cross referenced to the select component.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 52
Gives a total count of the nets in the netlist and when expancded it displays the nets in the project.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 53
When a net is selected it displays what the connections are. It also cross references to the layout and highlights the selected net in yellow.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 54
Single Node Nets list the same information as the Nets list but no cross referencing is done.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 55
Lists the Die component and part names.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 56
The Die Data displays the die width, height and thickness. The back bias, if supplied, is use for documentation purposes only. The die technology is either a Wire Bond or Flip Chip.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 57
The Pad Data like the Net List Data cross references to the Layout. All the information about the CBP and SBP are displayed and those in white can be edited in real time.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 58
This tool is used in the initial phase of designing an ASIC. It allows you to visualize the placement of the IO cells as well as the die and core dimensions and area.
The tool uses a spreadsheet CSV or TSV file for the input along with several other files that describe the cells in the pad ring and any filler or spacer cells that can or will be used in padding the ring.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 59
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 60
Celllist.dat: This file defines all the cells available to the tool including spacers and fillers of different widths that are used to pad a side of a die. F=Filler. S=Spacer
CellName,Width,PadCount,YOffset,XOffset,Type,,
PADIZ60_MO,60,1,28.5,30
DPAD,60,1,28.5,30
FSPCPD1,1,0,0,0,F
FSPCPD2,2,0,0,0,F
FSPCPD5,5,0,0,0,F
FSPCPD10,10,0,0,0,F
FSPCPD20,20,0,0,0,F
SPCPD01,0.1,0,0,0,S
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 61
Nnn.csv or nnn.tsv: Depending on your location, you may have English measurements (1200.5) or European measurements (1200,5). The .csv file is comma delimited whereas the .tsv file is tab delimited. This file defines the pad ring.
Side,PackagePin,BondPadNumber,PadName,InstanceName,CellName(,Comments)
T,,,,p37,IOCAP10
T,49,69,VDDREF_3.3,vddref_3.3,PVDD2DGZ,'VDDREF33'
T,,,,p38,IOCAP20
T,50,70,REF0,ref0pad,PCI66DGZ
T,51,71,REF1_FSC,ref1_fscpad,COMBOIO
T,,,,pi39,PFEED5_ISOVDDVSS_IO_COR
T,,,,pi40,PFEED5_ISOVDDVSS_IO_COR,'Changed'
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 62
PRELastSettings.ini: This file contains all the settings from the previously run project and is loaded automatically when the program is started.
An excel file can be generated and exported to Excel at any time using the Export to Excel feature for manual editing of the Pad Ring and then optionally imported back into the design. This makes an easy way to change the positions and number of cells on a given side.
The Create Cell List is a list of cells that need to be created used for the pick list under the Die Process Options section.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 63
This is where the project is set up. The input Database button is used to load the .csv or tsv file. The Work Directory will automatically be updated.
The Die Process Options defines how the pad ring will be built and sized. There are 2 options:
  Pad Sides with Fillers or User Dimensions.
  If the Pad Sides option is selected you need to pick a cell to use from the drop down list.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 64
The cells in the Using list come from the Create Cell List.
If User Dimensions is selected you supply the dimensions for the Die Width and Height.
The Ends and Center Options tell the tool where to place any filler cells that are added.
Other options define how the process runs.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 65
The Dimensions section defines the Bond Pad Width/Height to be used in the design The Corner Cell Width/Height is used to size the corner cells and as a result the IO cell height.
The ICED Pin Text Parameters are used to add pin text in the ICED tool. This is an external tool. (IC Editor)
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 66
The Lower Case define how the Cell and Instance Names will be handled. If checked they will be all lower case.
The Corner 1 Location tells where corner 1 will be placed and used if the Renumber Based On Corner 1 Location is checked. If the Freeze Corner 1 button is pressed the location of Corner 1 will be retained even if the die is rotated.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 67
The Process button starts with the Process Current CSV File option but can be changed using the Process menu to:
  Use Backup as Process Input File
  Backup CSV File than Process Data
  Using the backup file preserves the original file for repeated processing with changes in the parameters. When the file is processed a copy is automatically created and the original modified during the process.
The External tool interface is selected. Currently 2 tools are included:
  Astro
  AtopTech
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 68
The Die Origin defines the (0,0) origin of the die and resulting output coordinates.
The Thickness defines the thickness of the die and use in documentation.
The Back Bias is also used for documentation.
These parameters are used for documentation and added to the LIQ file which can be exported for use in the Wire Bond Explorer or 3D Viewer.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 69
The Stats section displays the result of the processing. The area can be shown in terms of Total Die area or the Core area.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 70
The Outputs tab contains 2 other tabs. One for the Astro output and the other for the AtopTech output.
You select which files you want output as well as the parameters required for the output.
The AtopTech tab has an optional Net List input function which is used to create cells that are in the Pad Ring but not in the netlist.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 71
Astro output parameters
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 72
AtopTech output parameters.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 73
Every time you execute a command it is recorded in a .kmd file. These commands can be executed at any time either by manually entering them in the command line or running the script using the Run command.
This is handy if you have set up parameters that you want to automatically run for every design.
The .kmd file can also be edited with lines you don’t want executed commented out with an “*” at the beginning of a line.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 74
The Ring View displays the results of the processing.
  Cells in Yellow are spacers.
  Cells in Green are Grounds.
  Cells in Red are Powers.
  Cells in Blue are Signals.
  Cells in Magenta are Fillers.
  The display can be changed to view the cells either filled or outlined and with or without colors. The color coding is handy for distribution analysis.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 75
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 76
As the cursor moves around the Pad Ring the statistics at the bottom of the screen below the command line change. If the cursor is placed on a pad that information will be displayed.
Cells can be swapped, moved, mirrored, deleted, and added.
The die can be rotated.
Pin one can be relocated and pads renumbered.
Cell types can be highlighted for location purposes.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 77
ASIC: Application Specific Integrated Circuit.
Base Die: The die that is placed on the substrate or PCB.
CBP: Component Bond Pad.
Die: An integrated circuit.
Die Attach Pad: The pad that attaches the die to the substrate or PCB.
DRC: Design Rule Check.
Fanout: Wire Bond connections from the die to substrate.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 78
LIQ: A Library Interchange file format description of the CBPs, SBPs, Wires, and Die Attach Pad.
LR: Inductance and Resistance.
PCB: Printed Circuit Board.
Pad Ring: The outer most portion of an integrated circuit made of IO cells and spacers.
SBP: Substrate Bond Pad.
Substrate: The surface to which the integrated circuit is attach.
Split Ring: A ring around the die with multiple isolated power or ground segments.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 79
Stacked Device: A device that is placed on the top of the Base Die.
Tier: A ring around the die used either as a Guide or Ring for SBP placement.
Wire Bond: The wire that extends from a CBP to a SBP or from a stacked device CBP to a Base Die CBP also known as a stitch.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 80
FastStart.pdf: This is the main reference document for the tools and includes many examples, demos and tutorials.
CommandList.pdf: Lists and explains the command language for the Wire Bond Explorer.
PRECommandList.pdf: Lists and explains the command language for the Pad Ring Explorer.
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 81
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top
Feature | Basic | Advanced | Full
Print Functions |  | * | *
Export to Excel |  | * | *
Data Sheet Generator |  | * | *
Data Source Links |  | * | *
File Preview |  | * | *
Import Die CSV |  | * | *
Export Die CSV |  | * | *
Export DXF Format |  | * | *
Shell to Pad Ring Explorer |  | * | *
Command Line Execution |  | * | *
FILIQAPLA command | * | * | *

## Slide 82
Feature | Basic | Advanced | Full
Scripting |  | * | *
Run Command Files |  | * | *
Function Keys |  | * | *
Die Attach Pad Editor |  | * | *
Quick Edit |  | * | *
Stacked Device Editor |  | * | *
Split Ring Editor |  | * | *
Bond Pad Editor | * | * | *
Load Netlist | * | * | *
Load Pin List | * | * | *
Load Die Picture | * | * | *
Import LIQ File | * | * | *
Save Project | * | * | *
Save Pin List | * | * | *
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top

## Slide 83
Feature | Basic | Advanced | Full
Export LIQ | * | * | *
License Manager | * | * | *
Tool Options and Settings | * | * | *
Die Editor | * | * | *
Wire Bond Editor | * | * | *
View / Zoom / Pan Functions | * | * | *
Project Properties | * | * | *
3D LIQ viewer |  | * | *
Pad Ring Explorer |  |  | *
AS2Pack Copyright 2011 by Prince Enterprises - Windy Top