## Slide 1: Library Builder
A unique combination of tools to explore and develop ASIC wirebond solutions
Notes: <number>

## Slide 2: Library Builder – Overview
Automatically generate DRC-correct wirebond fanouts
Up to four substrate rings supported
Multiple fanout patterns
Netlist or freehand driven
Back-annotation of changes and/or creation of netlist
Future releases will support stacked die
Can be easily used for single package designs or multi-component COB/PCB designs
Notes: <number>

## Slide 3: Library Builder – Overview
Multiple output formats (DXF, Gerber, GDS, ASCII)
Multiple input formats (BMP, TIFF, JPG, CSV (Excel), ASCII, DXF, GDS)
Interface with other tools by Prince Enterprises such as the Pad Ring Explorer
Notes: <number>

## Slide 4: Library Builder – Die with Wirebonds
Notes: <number>

## Slide 5: Supports Top-Down AND Bottom-Up Design
Top-Down
  Start with a defined die and netlist
    Die has already been defined or already exists
    Netlist to describe pin connections between die and package/PCB
  Develop wirebond fan-out pattern
    Drive package/PCB/assembly
Bottom-Up
  Start with an idea for a die
    Approximate size and aspect ratio
    Can interactively assign pins to sides of die
  Explore different die sizes and pinouts
    Examine complete product space tradeoffs
      Manufacturing costs
      Assembly costs
  Can generate a netlist/pinout from interactive exploration
    Drive pad-ring generation in ASIC P&R tool
Notes: <number>

## Slide 6: Industry-proven algorithms
Original code stream developed to assist MCM design house in the early 1990’s.
Second generation algorithms licensed to Mentor’s PADs and Synopsys’ Sager systems and are still in use today.
This third generation represents a complete rewrite of the algorithms to allow for a better user interface and integration of multiple tools into a single tool.
Notes: <number>

## Slide 7: Superior QOR (Quality of Results)
Patent Pending algorithm yields superior wirebond results
  Minimum total wirebond length
  Minimum wirebond angles
Algorithm places die bond pads into geographic groups based on distances between die bond pads and bonds out each group separately.
  Other tools center the substrate pads at the geometric center of each side and evenly spread out the pads regardless of gaps between die bond pads.
    Can lead to longer wirebonds
    Can create excessive wirebond angles
  Library Builder iteratively looks at multiple solutions and interactions between groups to generate the best final solution.
    Total Maximum Iterations can be set (defaults to 100) and the tool will stop before the max iterations if the changes between iterations is less than a set parameter (defaults to .01 micron)
Notes: <number>

## Slide 8: Die with bond pad gaps (typical tool solution)
Notice substrate pads centered creating needless wirebond angles and lengths
Notes: <number>

## Slide 9: Die with bond pad gaps (Library Builder solution)
Notice Library Builder solution generates minimum wirebond angles and lengths
Notes: <number>

## Slide 10: Typical Design Flow (1)
Set up work paths where design data resides
  Netlist, if any (connectivity between die and package/PCB)
  Die picture or database, if any (size and bond pad location info)
  Pin List, if any (pin names, side of die, etc.)
    Usually from component datasheet
Import Netlist
  If netlist not available, a single part netlist can be generated
    Add die data to the design manually, OR
    Read in a pin list
Notes: <number>

## Slide 11: Typical Design Flow (2)
Select part for creation
Read in picture of die corresponding to the part selected
  If no die picture available, create a Dummy die
Add pads to the die
  Read in pin list if available
  If pin list not available, hand enter die pad outlines and fill in the pad data in the Properties dialog
Notes: <number>

## Slide 12: Typical Design Flow (3)
Die with pads added
Notes: <number>

## Slide 13: Typical Design Flow (4)
Add the number and type of wirebond tiers to be used on the PCB/package
  Go to the Fanout tab and define the tier parameters in the Properties: Fan Out section
Notes: <number>

## Slide 14: Typical Design Flow (5)
Assign pads to tiers
  Use the Assign tool to assign pads to tiers
Notes: <number>

## Slide 15: Typical Design Flow (6)
Set up DRC rules for various wirebond and assembly rules
Notes: <number>

## Slide 16: Typical Design Flow (7)
Generate the Fanout pattern
  This can be done automatically, automatically and then modified, or completely manually
Notes: <number>

## Slide 17: Typical Design Flow (8)
Zoomed in look at wirebonds
  Notice that in this case, the pads on the substrate are round and in-line with the wirebonds. This can be changed to rectangular pads and/or the angle held to 0.
Notes: <number>

## Slide 18: Typical Design Flow (9)
Run various reports and check the design
  If OK, save data/design
  If not OK, modify some parameters and re-run the fanout generation OR hand edit to achieve desired results.
Export desired data
Exit the tool
Notes: <number>

## Slide 19: Appendix of Screen Shots
The following pages contains a number of screen shots to highlight the intelligence and flexibility of the tool.
Notes: <number>

## Slide 20: Menu/Dialog Box Picks Context Sensitive
Most operations have context sensitive menus
  Assists user with knowing where in the flow he/she is
  Prevents possible erroneous operations or out-of-order operations
Notes: <number>

## Slide 21: Example Die Editing Menu Picks
Notice some items grayed out or missing
Notes: <number>

## Slide 22: Example Fanout Menu Picks
Notice some items grayed out or missing
Notes: <number>

## Slide 23: Numerous Options Can Be Set
Options can be set interactively or through an initialization file.
Allows for customized work environment.
Session settings can be saved or cleared
Notes: <number>

## Slide 24: Extensive Netlist Analysis/Sorting Capabilities
Netlist analysis/sorting is extensive
  Useful to find/isolate netlist errors
  Can quickly determine if the number of pins are correct for a component
Notes: <number>

## Slide 25: Netlist Selection and Display
Displays netlist with no special sorting.
Notes: <number>

## Slide 26: Netlist Sorted by Net
Displays summary of each net.
Can quickly debug net connectivity.
Notes: <number>

## Slide 27: Netlist Sorted by Ref Des
Displays summary of each reference designator
Can quickly check the number of pins and nets on the pins for each component instance.
Notes: <number>

## Slide 28: Netlist Statistics
Displays overall netlist statistics.
Can quickly check the components used, the number of instances, and total nets.
Notes: <number>